## Slide 1: SuitSat-2
Lou McFadin
W5DID
May 2006

## Slide 2: Suit Diagram

## Slide 3: SuitSat-2 Mission and Capabilities
Primary mission
Voice messages Commemorating (TBD)
This includes audio greetings from
Energia, ARISS Europe, ARISS Canada, ARISS U.S.A. ARISS Japan
A CD ROM with photos contributed from schools around the world.
Secondary Mission
Testbed for systems planned for future Amateur radio satellites
Amateur operations
Packet ops
SSB Transponder
FM Cross band repeater
SSTV images of Earth and Station
Experiments (TBD-TSFR (This space for rent)

## Slide 4: The Proposed Plan
Build upon Suitsat-1 design
Re-use safety interlock circuit
Transmitter and Receiver module
IHU Module
Control Panel same as Suitsat-1
New Power module for solar panels
Solar Panels
Up to Four Experiments
Four Temperature Sensors
Up to Four cameras for SSTV
Modular design so that late subsystems can be deleted

## Slide 5: Future Concept Testbed
Use as a test bed for new concepts for future Amateur radio Satellites.
  Eagle power system
    Max power point converters for solar panel
    Distributed Converters
    Distributed Storage system
  Software Defined Radio (SDR) Prototype ?
  Backup off the shelf Tx/Rx design pursued in parallel
  Additional experiments

## Slide 6: SSTV
SSTV
  Four video ports (NTSC or pal by agreement)
  No power until switched on just before data take.
  Two U.S. Supplied
  Two Russian supplied
  No blank video
    Processor examines video and skips if no image present

## Slide 7: Experiments
Experiment ports
  Four ports
    One reserved for MicroChip (Supplier of electronics) non commercial.
    Three for other experiments
    Data packets to be 2k Bytes transferred on request from the IHU.

## Slide 8: Radio Module
Radio
Two paths
  SDR Eagle prototype
    Multimode
    SSB Crossband (U/V) Transponder repeater with Telemetry beacon
    FM-FM Cross band (U/V) packet
    Multiple signals simultaneously
  Simple Cross band Radio
    70 CM uplink 2M downlink
    2M FM voice and SSTV beacon

## Slide 9: Solar Power System
Could be an experimental Flexible Solar panel similar to that used by the U.S. military.
Could be a prototype of the Eagle Solar panel.
NASA supplied?
Russian supplied?
Power converter based on planned Eagle design.
  Designed to be placed in series with the surplus ISS batteries.
  Design such that if no Solar panel is available, it can be deleted and the batteries connected the same as Suitsat-1.

## Slide 10: Suitsat-1 Block Diagram

## Slide 11: Proposed Suitsat-2 Block Diagram

## Slide 12: Next steps for Suitsat-2
Define requirements
Define Tasks and
Define Schedule
  Mini TIM meeting in Houston in July
Funding ?