## Slide 1
An Introduction to Amateur Satellites
AMSAT
Barry A. Baines, WD4ASW
Vice President-Field Ops
AMSAT- North America

## Slide 2
AMSAT
Presentation Outline
A Simple Primer on Satellites
An Overview of the Amateur Satellite Program
Phase 3D-The Satellite for ALL Amateurs
Closing Remarks

## Slide 3
AMSAT
Satellite Primer

## Slide 4
AMSAT
What is a Satellite?
Like a Repeater
Retransmits what it “hears”
Has Optimized Receivers, Transmitters
Antennas
Great Location!
Enables Small Stations to Communicate Over Greater Distances

## Slide 5
AMSAT
What is a Satellite?
Unlike a Repeater
Has a Moving Footprint!
  Location Changes/Availability Varies
Frequency Alteration due to Doppler Shift
Full Duplex
  Uplink and Downlink on Different Bands Simultaneously
Multi-mode (CW/SSB/Digital)
“World Wide” Coverage

## Slide 6
AMSAT
Satellites Utilize “Transponders”
Receives a SEGMENT of One Band
Retransmits EVERYTHING It Hears on Another Band
Inverting Transponders
  Lowest Incoming Frequency is Retransmitted Over the Hightest Outgoing Frequency
  Inverts Signal (LSB to USB)

## Slide 7
AMSAT
A Wide Variety of Satellites Exist
18 Satellites Currently in Operation
Satellites Under Construction
  Phase -3D to be Launched by Ariane
  SUNSAT (South Africa)
  PANSAT (NPGS-Spread Spectrum)
  SEDSAT (UAB-Huntsville)
  TechSat-2 (Israel)

## Slide 8
AMSAT
Satellite Characteristics
Digital/Analog
Orbital Parameters
Frequencies Utilized
“Payload”

## Slide 9
AMSAT
Orbital Parameters
Eccentricity-How Circular the Orbit?
Apogee: Point Farthest to Earth
Perigee: Point Closest to Earth
Inclination Relative to the Equator
Keplerian Elements “Describe” the Orbit

## Slide 10
AMSAT
Satellite Systems
Attitude Control (RCS, Torquing Coils)
Central Computer (IHU)
Communications (Command Rcvr/Beacons/Ant)
Energy Supply (Batteries/Solar Panels/BCR)
EngineeringTelemetry (Electronic Sensors/Encoders)
Enviroment Control (Mechanical Design, Heat Pipes)
Guidance and Control (Sun/Earth Sensors)
Mission-Unique Equipment (Transponders/GPS/CCD)
Propulsion (Kick Motor/Arc Jet)
Structure
Most of the Development Effort Does Not Involve Amateur Radio

## Slide 11
AMSAT
36 Years of Amateur Radio in Space

## Slide 12
AMSAT
Project OSCAR
West Coast hams launch Project OSCAR in 1959 (Orbiting Satellite Carry Amateur Radio)
Launch opportunity on Discover XXXVI from Vanderburg AFB on 12 DEC 61
First satellite to be launched as a secondary payload from a primary launch vehicle and then enter a separate orbit.
Satellite weighed 10 lbs and built in basement/garages of the Project OSCAR team
  140 MW transmitter sent “HI” with cw rate based upon satellite temperature
Satellite transimitted telemetry for 22 days

## Slide 13
AMSAT
Overwhelming Success
More than 570 Amateurs in 28 Countries sent Observation Reports to the OSCAR Data Reduction Center
  Radio Propogation through Ionisphere
  Spacecraft Orbit
  Satellite Thermal Design
Project Demonstrated Amateurs Are Capable of:
  Design/Construction of Reliable Spacecraft
  Track Satellites
  Collect/Process Related Scientific and Engineering Information

## Slide 14
AMSAT
OSCAR II & III
Project OSCAR built OSCAR-II, similar in scope to OSCAR- I, launched 2 JUN 62 and lasted until 19 JUN 62. Operated 100mw Transmitter
OSCAR- III become the first Amateur Radio to carry a transponder
  50 KHz wide uplink near 146 MHz
  Downlink near 144 MHz
  1 Watt output
OSCAR-III, launched 9 MAR 65, lasted 18 days with 1,000 amateurs in 22 countries operating through it.
  Demonstrated ‘Free Access’ and ‘Multiple Access’

## Slide 15
AMSAT
OSCAR-IV
TRW Amateur Radio Club
OSCAR IV launched 21 DEC 65 by Titan III-C which had a top stage launcher failure and did not achieve geostationary orbit
30 lb satellite Ended up in a Highly Elliptical Orbit
First Solar Powered Amateur Satellite
First Multiband Satellite (2M uplink/70 CM Downlink)
Operated for 85 days before failure/fell into Atmosphere on 12 APR 76

## Slide 16
AMSAT
Birth of AMSAT
Project OSCAR Languishes Following OSCAR-4
Members of DC Area Ham Radio Clubs affiliated with Government Agencies, Communications Companies, and Labs, meet in Late 1968 in the home of George Jacobs, W3ASK
Goal is to Revitalize the Amateur Satellite Program
Radio Amateur Satellite Corp. was chartered on 3 MAR 69 in the District of Columbia as 501(c)(3) organization

## Slide 17
AMSAT
OSCAR-5
First AMSAT project was to assist with OSCAR- 5, developed by University of Melbourne, Australia
First NASA Launch for AMSAT on 23 JAN 70
Telemetry beacons at 29 MHz and 144 MHz
First Ground Controlled Amateur Satellite-Command Receiver to control 29 Mhz Beacon
No Solar Cells/Battery Operated
Magnetic Attitude Stablizing System
Telemetry with 6 Type of Data Operated 52 Days

## Slide 18
AMSAT
OSCAR-6
OSCAR-6 Was First of the “Phase 2” Satellites
Multinational Effort (US-West Germany-Australia)
Launched 15 OCT 72 with a Weather Satellite
2 Meter Uplink/29 MHz Downlink
Telemetry Beacon with 24 Types of Data on Satellite
Uplink Control with 35 different Commands
International Ground Stations
Operated 4.5 Years/ Still in Orbit

## Slide 19
AMSAT
OSCAR-7
Launched 15 NOV 74
First Time There were Two Working Amateur Satellites in Orbit
Two Transponders (146/29 and 432/146 MHz)
First satellite-to-satellite Comm linkup in History
Multinational Satellite (US-Australia-Canada)
2.304 MHz 100 mw beacon never used as FCC denied permission
Operated 6.5 years/still in Space

## Slide 20
AMSAT
OSCAR-8
OSCAR-8 launched 5 MAR 78 from Vanderburg AFB
Two Transponders
Multinational--Japan, US, Canada, and West Germany
Worked until mid-1983 when Batteries Died

## Slide 21
AMSAT
UoSAT-9
UoSat-9 was First Amateur Satellite Built by Great Britain (University of Surrey)
Launched 6 OCT 81
115 lb. satellite placed in 340 Mile High Orbit
Transmitted Data and CCD Pictures
Contained magnetometer and radiation/particle detectors
Synthesized Voice Radio with 150-word Vocabulary
Beacons on 7, 14, 21, 28 MHz and 2 and 10 GHz for Propogation Studies
Returned to Atmosphere 13 OCT 89

## Slide 22
AMSAT
AO-10
AO-10 First of the Phase-3 Satellites
Launched 16 JUN 83/200-lb clone to Phase-3A which was destroyed in Second Launch of Ariane-3 Vehicle
Built by West Germany, US, Canada, Hungary, Japan
Molynia Type Orbit, Longer View Time, Higher Frequencies
Launched 16 JUN 83
Ariane Bumped Spacecraft upon Separation, Damaging Antennas and caused Spinning
When Thruster was Ignited on 11 JUL 83, did not turn off as Ordered and was placed in 50% Higher Orbit than Planned
Still in Use when in Sunlight

## Slide 23
AMSAT
OSCAR Satellite Summary
Satellite Launch Service Life
OSCAR-I 12 DEC 61 22 Days
OSCAR-II 2 JUN 62 19 Days
OSCAR-III 9 MAR 65 18 Days for Transponder
OSCAR-IV 21 DEC 65 85 Days
OSCAR-5 23 JAN 70 52 Days
OSCAR-6 15 OCT 72 4.5 Years
OSCAR-7 15 NOV 74 6.6 Years
OSCAR-8 5 MAR 78 5.3 Years

## Slide 24
AMSAT
OSCAR Satellite Summary
Satellite Launch Service Life
UO-9 6 OCT 81 8 Years
AO-10 16 JUN 83 In Service
UO-11 2 MAR 84 In Service
FO-12 12 AUG 86 5 NOV 89
AO-13 15 JUN 88 5 DEC 96
UO-14 22 JAN 90 Commercial Service
UO-15 22 JAN 90 23 JAN 90
AO-16 22 JAN 90 In Service
DO-17 22 JAN 90 In Service
WO-18 22 JAN 90 In Service
LU-19 22 JAN 90 In Service
FO-20 7 FEB 90 In Service

## Slide 25
AMSAT
OSCAR Satellite Summary
Satellite Launch Service Life
AO-21/RS-14 29 JAN 91 3.6 Years
UO-22 17 JUL 91 In Service
KO-23 10 AUG 92 In Service
KO-25 26 SEP 93 In Service
IO-26 26 SEP 93 In Service
AO-27 26 SEP 93 In Service
PO-28 26 SEP 93 Commerical Service
FO-29 17 AUG 96 In Service
MO-30 5 SEP 96 Dead Uplink Rcvr

## Slide 26
AMSAT
RS Satellite Summary
Satellite Launch Service Life
RS-1 26 OCT 78 Few Months
RS-2 26 OCT 78 1981
Iskra-1 10 JUL 81 7 OCT 81
RS 3 17 DEC 81 2 Years
RS-4 17 DEC 81 2 Years
RS-5 17 DEC 81 6.5 Years (1988)
RS-6 17 DEC 81 3 Years
RS-7 17 DEC 81 6.5 Years (1988)
RS-8 17 DEC 81 4 Years

## Slide 27
AMSAT
RS Satellite Summary
Satellite Launch Service Life
Iskra-2 19 AUG 82 9 JUL 82
Iskra-3 18 NOV 82 16 DEC 82
RS-9 Flight Cancelled
RS-10/11 23 JUN 87 May 97
RS-12/13 5 FEB 91 In Service
RS-14/AO-21 29 JAN 91 JUN 94
RS-15 26 DEC 94 In Service
RS-16 4 MAR 97 In Service

## Slide 28
AMSAT
OSCAR Program Phases
Phase I: Low Earth Orbit, short lifetime, primarily beacon-oriented satellites
  OSCARS 1 -3, Russian Iskra 1-2
Phase II: Higher Orbits than Phase I (LEO), much longer lifetimes
  Analog: OSCARS 6-8,
  Digital: UO- 9,11
Phase III: Highly elliptical Molyna-type orbits offering higher access time, power and more diverse communication transponders
  OSCARS 10, 13, and Phase 3D

## Slide 29
AMSAT
Satellite Categories
EASY Birds
  RS Satellites: RS-11/12, RS-15, RS-16 (Russia)
  Manned Satellites (MIR/SAREX)
  Dual Use: FO Satellites (Japan)/AO-27 (FM)
Digital Satellites
  Primarily “Store and Forward” Bulletin Boards
  Other Payloads (Cameras/Sensors)
  PSK Mode (AO-16, WO-18, LU-19)
  9600 DFM (UO-12, KO-23, KO-25)
  1200 AFSK (UO-11, MIR, DO-17 Downlink Only)
DX Satellites
  AO-10
  Phase-3D

## Slide 30
AMSAT
Digital Satellites
The Fastest Growing Area of Satellite Activity
Almost Every Satellite Launched or Currently Under Construction has Digital Capability
Continious Time in Use (Due in Part to Ground Station Automation)

## Slide 31
AMSAT
Digital Satellites
Most Versatile Use as Computers and Users “Go Digital”
  Types of Data Forwarded
  Rapid Growth of No Code Techs Who Are Interested in Digital
  High Degree of Technical Growth as Shift to Higher Baud Rates Occurs
  Evolution of Ground Based ‘Servers’ Changes Information Flows
  Digital Transponders (AO-27, Fuji Sats)

## Slide 32
AMSAT
Common Digital Characteristics
Satellites Are Relatively Small
  Microsats Proved Concept “Small is Beautiful”
  Low Powered with Relatively Small Data Storage
  Multiple Satellites Launched on Same Vehicle
Polar Orbit Utilized to Provide WorldWide Coverage
Covers the Whole Globe 4 to 6 Times/Day
Relatively Easy to Launch/No Station Keeping

## Slide 33
AMSAT
Common Digital Characteristics
Utilizes Specialized Software for Uploading and Downloading Files (PACSAT Protocol)
Ability to Handle 2 Uploads/10 Download Requests Simultaneously
All Stations Store Transmitted Data and Request Only What They Don’t Already Have

## Slide 34
AMSAT
Digital Ground Stations
Computer with Appropriate Software
  WISP, WISP-32, Satsked, PB/PG
  Sat callsigns/Station Callsign,TNC Config
Satellite Tracking System (Lat/Long, Rotor, Radio Interface)
Data Compression/Decompression (PKZIP, LHA)
Installation of Modem Hardware (DFM/PSK)
Modified Radios for 9600 DFM

## Slide 35
AMSAT
The AMSAT Approach to Satellite Development

## Slide 36
AMSAT
International Scope
Affiliate organizations in other countries
Cooperation on individual projects
An organization defines basic spacecraft and interface requirements
Teams are formed from international ‘pools’ for various systems/subsystems

## Slide 37
AMSAT
International Cooperation
Phase-3D has components from 13 countries
  Russia Propellant Tanks
  Japan SCOPE Cameras
  UK 2M Xmtr/Aux. Batteries
  Finland 10 GHz Xmtr
  Czech Republic Receivers
  USA Space Frame/GPS/RUDAK
  Germany 70 CM Xmtr/LEILA/Project Mgr.
  Canada Radiation Testing
  Belgium 146/435/2400 MHz Rcvr
  Hungary Battery Charger Regulators
  Slovenia 21 MHz/5.7 GHz Rcvr
  France 1.2 GHz Ant./Test Support-SBS
  New Zealand Machine Parts

## Slide 38
AMSAT
Building Satellites ‘on the Cheap’
AMSAT depends primarily on volunteers
Only one full time employee (office manager)
KISS Approach to satellite design/’home brew’
Parts donations from corporate sources
Systems built in garages/basements
Develop university relationships (Weber State)

## Slide 39
AMSAT
Launch Opportunities
Most Satellites Ride into Orbit as an Extra Passenger on a Government/Commerical Agency’s Booster
AMSAT has Developed Innovative Designs to make available ‘unusable’ space in launch vehicles
  Example: 1990 launch of Microsats on Ariane IV
AMSAT will Trade Knowledge, Skill, and Manufacturing Capacity for a Reduction/Waiver of Launch Costs
  Example: SBS for P3D on Ariane V

## Slide 40
AMSAT
Launch Opportunities
Take Advantage of Test Launches w/Inherent Uncertainties
  ex: Ariane III and Ariane V
Launch Insurance NOT Normally Purchased
Cover Risk by duplicating components, such as Spaceframes

## Slide 41
AMSAT
Cleanliness/Quality Control
AMSAT spacecraft are designed for safe, contaminant free and reliable operation
No AMSAT satellite presented to a launch agency has ever been rejected for lack of cleanliness or contaminated parts

## Slide 42
AMSAT
Cleanliness/Quality Control
Clean room facilities may be ‘home brewed’ or donated (such as the P3D cleanroom)
Spacecraft are subjected to most of the same tough enviromental and thermal tests as commerical/military spacecraft
“Shake and Bake” Time in commercial or governmental facilities often donated to AMSAT during “off peak” periods for testing

## Slide 43
AMSAT
PHASE-3D
AMSAT’s Most Ambitious Project
“The Satellite For ALL Amateurs”

## Slide 44
AMSAT PHASE 3-D
History
Invitation from ESA to Ride on New Ariane 5 Booster
Build Around Unused Space on Ariane 5 Upper Stage
AO-13 Orbital Studies Showed De-Orbit in 1995-1996
Team Formed May 1990

## Slide 45
AMSAT PHASE 3-D
Main Features
International in Scope
Most Sophisticated and Expensive Ham Satellite Ever
Uses Ham Satellite Bands from 21 MHz to 24 Ghz
High Gain Antennas and Powerful Receivers
600 Watt Power Budget
High Inclination Elliptical Orbit

## Slide 46
AMSAT PHASE 3-D
Specifications
ORBIT: High Molniya 29,000 Miles X 2400 Miles
ORBITAL PERIOD: 16 Hours Planned
RECEIVE: 21, 145, 435, 1269, 2400 and 5660 MHz
TRANSMIT: 145, 435, 2400, 10450, 24040 MHz
IF MATRIX: Cross Link any Receiver to any Xmitter
TV CAMERAS: 2 Earth-Imaging, digital downlink on 2400 MHz

## Slide 47
AMSAT PHASE 3-D
Receivers (Earth > Satellite)
21.210 - 21. 250 MHz
145.800 - 145.990 MHz
435.300 - 435.800 MHz
1268.075 - 1268.575 MHz
1269.000 - 1269.250 MHz
2400.100 - 2446.700 MHz
2446.200 - 2446.700 MHz
5668.300 - 5668.800 MHz

## Slide 48
AMSAT PHASE 3-D
Transmitters (Satellite > Earth)
145.805 - 145.990 MHz
435.475 - 436.200 MHz
2400.225 - 2400.950 MHz
10.451025 - 10.451750 GHz
24.048025 - 24.048750 GHz

## Slide 49
AMSAT PHASE 3-D
Transmitters (Satellite > Earth)
145.805 - 145.990 MHz
435.475 - 436.200 MHz
2400.225 - 2400.950 MHz
10.451025 - 10.451750 GHz
24.048025 - 24.048750 GHz

## Slide 50
AMSAT PHASE 3-D
Specifications
APPROXIMATE WEIGHT: 800 Pounds Planned
APPROXIMATE DIAMETER: 7.5 Feet
APPROXIMATE WINGSPAN: 20 Feet
ANTENNA GAIN: 4 TO 19 Dbic (Typical)
STABILIZATION: Three Axis (Always Pointing to Earth)
TRANSMIT POWER : 40 to 250 Watts PEP (Typical) (Up to 10-20 Kilowatts EIRP)

## Slide 51
AMSAT PHASE 3-D
Specifications
INTERNAL HOUSEKEEPING: AO-13 Architecture
RUDAK: Store and Forward/Digipeater/Gateway Storage of CCD Pictures-- Dual CPUs with 2 x 16 Megabytes storage
RUDAK MODES: 1200 PSK/9600 FSK modems @ up to 38.4 kbps -- Dual DSP modems @ up to 56 kbps
LAUNCH OPPORTUNITY: 1997 (?)
LAUNCH LOCATION: Kourou, French Guiana
PROPULSION: 400 Newton Kick Motor/Arc Jet

## Slide 52
AMSAT PHASE 3-D
Specifications
POSITIONING: On-Board GPS Receiver/ Sun and Earth Sensors
ANTENNA DESIGN: Patch Antennas/ Quarter Wave and Folded Dipoles/ Small Dishes
THERMAL CONTROL: Internal Heat Pipes
BATTERIES: Nickel-Cadmium Technology

## Slide 53
AMSAT PHASE 3-D
Cost
APPROXIMATE ESTIMATE: $4.5 Million
AMSAT-NA PORTION: $1.8 Million
SOURCES: Primarily From Individual Amateur Radio Operators

## Slide 54
AMSAT PHASE 3-D
Current Status
Carrying Structure Construction Complete
Spacecraft Structural Modifications Ongoing
Final Spacecraft Integration Completed in August
Final Environmental Testing in August/September

## Slide 55
AMSAT PHASE 3-D
Launch Status
Based on Data from Ariane 501, ESA has Infomed AMSAT of Significantly Higher Estimates of Acceleration and Vibration Enviroment of Spacecraft Riding on 502 .

## Slide 56
AMSAT PHASE 3-D
Launch Status
Based on ESA’s Revised Estimates, AMSAT has Re-evaluated the Structural Capabilities of P-3D
  An Independent Structural Engineer Has Reviewed P-3D’s Design and Construction
  His Report Recommended a Number of Structural Modifications to Increase the Spacecraft’s Vibration and Acceleration Capability
Spacecraft Modifications Were Made Over the Last Four Weeks

## Slide 57
AMSAT PHASE 3-D
Launch Status
AMSAT-DL has Informed ESA that the Need to Make Structural Modifications Would prevent AMSAT from Delivering P-3D to Kourou by ESA’s August 10 Deadline
ESA Does Not Currently Contemplate P-3D Flying on 502 Unless Something Changes to Their Schedule
In the Absence of P-3D, AMSAT May Need to Provide the Planned Mass Simulator
If needed, Simulator to be in Kourou by September 5

## Slide 58
AMSAT PHASE-3D
Launch Status
Will Ariane 502 fly in September?

## Slide 59
AMSAT PHASE 3-D
Launch Status
Some Expectation that 502’s Schedule Will Slip
Should Schedule Slippage Occur and P3D schedule Becomes Compatable with 502’s, Efforts will be Made to Substitute P-3D for the Mass Simuilator
AMSAT Continues Work to Complete Phase-3D and Conduct Enviromental Testing

## Slide 60
AMSAT PHASE 3-D
How Can I Help?
Join and Support AMSAT!
Contribute to the Phase 3-D Fund
Corporate Donations
Foundation Grants

## Slide 61
AMSAT
Closing Thoughts
AMSAT Continues to Push the Technological Envelope
AMSAT’s Contritubution to Amateur Radio
  Expansion into the Microwave Frequencies
  Higher Digital Baud Rates
  Variety of Modes
AMSAT’s Scientific and Educational Objectives
AMSAT’s KISS Approach is being followed by Others