## Slide 1
AMSAT
Radio Amateur Satellite Corporation
Steve Park WB9OEP
AMSAT Area Coordinator

## Slide 2
Who is AMSAT?
What's Up?
How do I get there?
What's next?
How do I find out more?
Steve Park WB9OEP
AMSAT Area Coordinator

## Slide 3: Who is AMSAT?
A Non-profit Corporation with an elected Board of Directors
One paid employee and thousands of volunteers
Amateur Satellite Operations
    User Support
    Software Exchange
    AMSAT News Service
    AMSAT Journal
Satellite Engineering
    Propose, develop, deploy and operate Amateur Satellites

## Slide 4: WHAT'S UP ???
Analog Satellites
    AMSAT OSCAR 10 Old Faithful!
    AMSAT OSCAR 13 The "Cadillac" of OSCAR's
    Radio Sputnik 10/11 Two meters up and 10M down
    Radio Sputnik 12/13 Modes A and K are alive and well!
    Radio Sputnik 15 Modes A and K are alive and well!
    FUJI OSCAR 20**
Digital Satellites
    PACSAT OSCAR 16 DOVE OSCAR 17
    WEBERSAT OSCAR 18 LUSAT OSCAR 19
    UoSAT OSCAR 22 KITSAT OSCAR 23
    KITSAT OSCAR 25 ITAMSAT OSCAR 26
    AMRAD OSCAR 27 ** PoSAT OSCAR 28

## Slide 5: WHAT’s UP ???
Just Added
    FO-29 (AMSAT-JA) FO-20 replacement launched Aug. 17, 1996
    UNAMSAT2 (AMSAT-XE) Meteor Sounder launched September 5, 1996
Experimental
    UoSAT OSCAR 11 Educational and scientific stalwart
    UoSAT OSCAR 14 Highly experimental PACSAT
Manned Spacecraft
    MIR Spacestation Two meter rigs smuggled into space
    Now w/ Repeater Space AmateurFunk EXperiment (SAFEX)
    SAREX Shuttle Amateur Radio EXperiment
Since OSCAR 1 in 1959, AMSAT has over 37 years of service to the Amateur Satellite Service

## Slide 6: How do I get there?
Where are you going?
    Fone, CW, DXing, ragchewing
    Packet, remote imaging,...
The “Repeater in the Sky”

## Slide 7: The Repeater in the Sky
Ionosphere
Shortwave
VHF, UHF and Microwave
Ever use a repeater with an 800 mile high antenna?

## Slide 8
Nice view from up here!!!

## Slide 9: Differences
Satellite Transponder
  Wide bandwidth (800 kHz)
  Multi User
  Cross Band
  Linear (SSB, CW)
  Moves
  Low Power Transmitter
Satellite BBS
  Full Duplex
  Crossband
  1200 bps PSK
  Battery Power
  Moving
Terrestrial Repeater
  Narrow bandwidth (15 kHz)
  Single User
  Single Band
  Non-linear (FM)
  Stays in one place
  High Power Transmitter
Terrestrial Packet BBS
  Simplex
  Single band
  1200 bps FM (AFSK)
  Commercial Power
  Stationary

## Slide 10: How do I get there?
What do you have to work with?
    Mode A equipment: omnis, 10M Rx and 2M Tx
    Handheld 2 meter rig
    RS10/11, RS12/13, RS15, DOVE, AO27
10m Rcvr
2m Xmtr
Dipole
Whip or Ground Plane
10 Watts

## Slide 11: How do I get there?
2m FM Tx
70cm SSB Rx
Modem
Satellite Packet on the “PACSAT’s”
    Store and Forward BBS in the sky
    1200 PSK and 9600 FSK

## Slide 12: How do I get there?
When and where are the birds?
    Tracking and orbit software
TRACKING SATELLITE AO-13 FOR WB9OEP FROM EPOCH 23AUG95 025002
DATE Time Az/El Lng/Lat Range/ Ph/Md PA/E/V Dop. ES SSE
23AUG95 070612 278/58 109/ 28 16772/ 27/B 56/0/V -1540Hz 17 40
23AUG95 071612 269/59 108/ 25 18641/ 31/B 50/0/V -1487Hz 15 36
23AUG95 072612 262/59 108/ 22 20437/ 34/B 45/0/V -1424Hz 14 33
23AUG95 073612 257/57 109/ 19 22153/ 38/B 41/0/V -1358Hz 13 31
23AUG95 074612 252/56 110/ 17 23787/ 42/B 38/0/V -1291Hz 13 29
23AUG95 075612 249/54 111/ 14 25339/ 46/B 35/0/V -1226Hz 12 27
23AUG95 080612 247/52 112/ 12 26813/ 49/B 32/0/V -1163Hz 11 26
23AUG95 081612 245/50 113/ 10 28211/ 53/B 30/0/V -1103Hz 11 24
23AUG95 082612 244/47 114/ 9 29535/ 57/B 27/0/V -1045Hz 11 23
23AUG95 083612 244/45 116/ 7 30790/ 61/B 25/0/V -989Hz 10 22
0=RETURN,1=CONTINUE,2=SCROLL,7=STEP1,8=WINDOW

## Slide 13
Insert Beginners Guide Handouts...

## Slide 14: Four Phases of AMSAT Programs
Phase 1: Battery powered and sub-orbital satellites
Phase 2: Low Earth Orbits (LEO's)

## Slide 15: Low Earth Orbits
Earth
N
S
Circular Orbits
Polar (incl. = 90 deg.)
300 to 800 miles high
5 to 10 useable orbits/day
15 to 25 minutes access
1000 km

## Slide 16
Insert Microsat Project Here...

## Slide 17: EUROMIR 95
SAFEX II : Space Amateur Funk EXperiment
Regular MIR 2meter operations
70 cm equipment
  FM voice
  FSK 9600 baud packet modes (G3RUH system).
Picture transmission by means of a new "SSTV" mode.
  AX.25 packets
  "thumbnail" image over a short period of time
  increasing resolution as more of the transmission is received.
Landing in Kazakhstan on 16-Jan-96.

## Slide 18: EUROMIR FREQUENCIES
2m-Band -------
  Voice: Downlink 145.850 MHz
  Uplink 145.250 MHz
  Packet Radio: Downlink 145.550 MHz
  Uplink 144.625 MHz 145.550 MHz
  addtional Uplinks: 145.200 145.225 144.675 144.725 MHz
70cm-Band ---------
  Voice: Downlink 437.925 MHz
  Uplink 435.725 MHz
  Packet Radio: Downlink 437.775 MHz
  Uplink 435.775 MHz
  additional Uplinks: 435.800 MHz to 436.000 MHz with 25 kHz spacing

## Slide 19: Four Phases of AMSAT Programs
Phase 3: High Earth Orbits (HEO's)

## Slide 20: High Earth Orbits
Earth
N
S
Elliptical Orbits
20 to 60 deg. incl.
up to 26,000 miles high
2 useable orbits/day
4 to 8 hours access
40,000 km

## Slide 21: How do I get there?
HEO equipment
    Antenna Gain and Tracking
2m SSB Rx
70cm SSB Tx
Low Loss
Coax
Low Loss
Coax
2m Beam
435 Beam
Elevation
Rotor
2m Preamp
Azimuth
Rotor
Tripod

## Slide 22
Insert AO-13 stuff here

## Slide 23: Mean Anomaly & Scheduling
Earth
N
S
Perigee
MA= 0
time = 0
Apogee
MA=128
time = +6
time = +1
time = +2
time = +3
time = +4
time = +5
time = +7
time = +8
time = +9
time = +10
time = +11

## Slide 24: What Does it Sound Like?
Just another ham band
    Similar to SSB or CW on any band
    Signals are 3 to 4 S units above the noise
    Continuous tuning and calling CQ
    Lots of ragchewing, DX chasing, etc.
NOT Just another ham band
    Full Duplex operation -- “I can hear myself!”
    No Alligators-- Loud signals are discouraged.
    The best of the courteous and skilled operators

## Slide 25: What will I find??
The Gentlemans Bandplan for OSCAR 13
    WAC, WAS, DXCC,
    Field Day, JOTA, K2ZRO tests
General Beacon
PSK, RTTY, CW
DX Net
Engineering
Beacon
145.812
145.890
145.950
145.985
AMSAT
Net
UK
Net
RTTY
Packet
SSTV
CW
DX Fone
Ragchews

## Slide 26: Other Activities
Operating Awards
    Worked All Continents
    Worked All States
    DXCC
    K2ZRO Technical Achievement
Operating Events
    Field Day
    Straight Key Night
    Radiosport
Telemetry and Remote Sensing
    Monitor the spacecraft operations
    Retrieve pictures and data from space

## Slide 27: WHAT'S ON THE HORIZON ???
SUNSAT (AMSAT-SA) "Parrot FM repeater" and Mode-S
VoxSAT (AMSAT-LU)
TM-Sat (Thailand) Another UoSat
SEDSAT (U of A Huntsville) Tethered launch from STS
PANSAT Naval Postgraduate School, Monterey, California
TechSat-2 Israel Technion Institute of Technology
Maëlle AMSAT-France
SAREX (AMSAT-NA) The Shuttle experiments continue...
SQUIRT Satellite QUIck Research Testbed, Stanford Univ.
KITSAT-3 Korean
HUTSAT Helsinki University of Technology, Finland

## Slide 28: WHAT'S ON THE HORIZON ???
Bad News - AO13 to re-enter in December of 1996
The “Chicken Little” contest has begun.
Last chance to use this marvelous bird.
Good News - Phase 3D to fly on Ariane 5 in May of 1997
The newest high-powered "Rolls-Royce"
Highly Elliptical Harmonic Orbit
Global AMSAT project
Built in Florida

## Slide 29: Phase 3D: A New Era
“The Rolls Royce”

## Slide 30: Phase 3D: A New Era
“More Power” and Antenna Gain for Phase 3D vs. AO-13
So What ??
Downlink Band AO13 P3D
        Xmtr Power/Ant Gain Xmtr Power/Ant Gain
2m (146 MHz) 50W/5.5dB 200W/11dB
70cm (435 MHz) 50W/9.5dB 250W/15.3dB
13cm (2.4 GHz) 1W/9dB 50W/19.5dB
3cm (10 GHz) -- 50W/20dB
1.25cm (24 GHz) -- 1W/20dB

## Slide 31: Phase 3D: A New Era
The Harmonic M/N = 3/2 Orbit
    > 20 hours per day availability
    Little or no tracking required
So What ??

## Slide 32: Phase 3D: A New Era
A New Approach
145.800-145.975 MHz
435.200-435.700 MHz
436.000-436.500 MHz
1269.00-1269.50 MHz
1268.50-1269.00 MHz
2400.xxx MHz
5.645 GHz
LEILA
LEILA
LEILA
LEILA
LEILA
24 GHz
10.4510-10.4515 GHz
2400.5-2400.9 MHz
435.300-435.700 MHz
145.800-145.975 MHz
UPLINK Receivers
DOWNLINK Tx
IF Matrix
(10.7 MHz, -15 dBm)

## Slide 33: Phase 3D: A New Era
The various bands will be designated as shown
"Mode B" will become "Configuration U/V"
Combinations such as "Config. UL/VSX” are possible.
Transponder Matrix
Band Uplink Downlink
15m (21 MHz) H None
10m (28 MHz) None T
2m (146 MHz) V V
70cm (435 MHz) U U
23cm (1260 MHz) L None
13cm (2.4 GHz) S S
5cm (5.6 GHz) C None
3cm (10 GHz) None X
1.25cm (24 GHz) None K
P3D Band Designations

## Slide 34: Phase 3D: A New Era
Antenna Configurations
Band Antenna Type Gain
10m (28 MHz) 2 ele. whip 4.5 dBi
2m (146 MHz) 3 low profile dipoles 10 dBic
70cm (435 MHz) 6 ele. patch array 13 dBic
23cm (1260 MHz) Short backfire 15 dBic
13cm (2.4 GHz) Parabolic dish 18 dBic
5cm (5.6 GHz) Parabolic dish 18 dBic
3cm (10 GHz) Dual horns 20 dBic
1.25cm (24 GHz) Horn 20 dBic

## Slide 35: Phase 3D: A New Era
“LEILA” - The Alligator Eater
Tunable Filter
& Detector
+
Tunable Notch Filter
To/From IHU
Synthesizer
IF Input
10.7 MHz
BW = 512 kHz
IF Output
10.7 MHz
9
4

## Slide 36: Phase 3D: A New Era
Three Axis Stabilized
  Reaction Wheels
  Deployed solar arrays
  Heat Pipes
Arc Jet Thruster... The cure for Chaos
GPS Receivers
  Location, Time and Frequency Reference
  Attitude Determination
“Made in Florida”
Other Features

## Slide 37: Hey, What about...???
SEDSAT B "To the Moon Alice"
SPACESTATION Wanna make a bet?
MARS-A and SOLAR SAIL The extra-terrestrials...

## Slide 38: HAM RADIO TO MARS
"Mars Global Surveyor" in late 1996
  The Jet Propulsion Laboratory in Pasadena, California
  Replacement for the ill-fated "Mars Observer"
  Many experiments carried on the spacecraft
1.3 watt CW beacon on 437.100 MHz.
  OSCAR satellite groundstation capable
  While enroute to Mars.

## Slide 39: HOW DO I FIND OUT MORE ???
Background
    Radio Amateurs Handbook
    Satellite Experimenters Handbook
    Columns in QST, CQ, QEX, etc.
    http://www.amsat.org
Join AMSAT
    AMSAT Journal Subscription
    AMSAT News Service on Packet and Internet
    AMSAT Nets - Tuesday 9:00 PM Eastern on 3840 kHz
    Houston Area AMSAT Net rebroadcast locally by AJ1R/KD4KSI Rptr System
Local Area Coordinators
    Steve - WB9OEP
    And many, many more!!!

## Slide 40: 13th AMSAT-NA Annual Meeting and Space Symposium
October 6-8, 1995
Orlando, FL. --International Airport Holiday Inn
P3D Updates, Papers and tours of the Integration Facility
Registrations still available -- Call Martha