## Slide 1
Satellite Tracking
Barry A. Baines, WD4ASW
VP-Field Operations
AMSAT-NA

## Slide 2
Why Track?
Satellites are Moving Transponders
Need to Predict When the Satellite Will be in View of Your Station
Antenna Pointing/Doppler Correction
May Want to Know When Mutual Pass Will Occur with Another Station

## Slide 3
Satellite Tracking
Need to be Able to Describe a Satellite’s Orbit
Data on Each Satellite is Unique
Orbital Characteristics Change Over Time
Various Sources of Data

## Slide 4
Satellite Orbits
An “Orbit” is the ‘highway’ on which a satellite travels around the Earth
The Type of Orbit Determines how the Satellite Can be Utilized
The higher the Orbit, the larger the “Footprint” and the Longer the Orbit

## Slide 5
Keplerian Data
“Keps” are the Variables Which Describe a Satellite’s Orbit
Keps are Developed by NORAD/NASA
  AMSAT Provides Reformatted Data
Keps are Distributed Worldwide
  Packet Bulletin Boards
  BBS (DRIG, NASA, AMSAT BBS’s)
  Web Sites (AMSAT)
  Automatic e-mail receipt from keps@amsat.org

## Slide 6
Keplerian Data
EPOCH is the time at which the snapshot is taken. Usually described by Year-Julian Date-Fraction of Date.
Inclination is the angle of the orbital plane with respect to the Equatorial Plane.
  0 degrees is an equitorial orbit
  90 degrees is a polar orbit
  Describes the maximum Northerly and Southerly Latitudes Over Which the Satellite Will Overfly

## Slide 7
Keplerian Data
Right Ascension of Ascending Node (RAAN) specifies where the satellite crosses the Equator on an Ascending (South-North) Node.
  Measured using an Astronomical Coordinate System which does not spin with the Earth
  Reference Point is Where Right Ascension is Defined as Zero (Vernal Equinox)
  An angle measured at the center of the Earth, Eastward from the Vernal Equinox to the Ascending Node

## Slide 8
Keplerian Data
Argument of Perigee is the Angle from the Ascending Node to Perigee in the Direction of Orbital Motion
  Perigee is the point where the satellite is closest to the Earth
  If ARGP=0, perigee occurs at the same place as the Ascending Node
  If ARGP=180, apogee (The point where the satellite is furthest from Earth) occurs at the same place as the Ascending Node

## Slide 9
Keplerian Data
Eccentricty is the Orbital Shape
  e=0 when the orbit is a circle
  e=1 when the orbit is highly elliptical
Mean Motion provides a measure of the size of the orbital ellipse
  Kepler’s Third Law provides a relationship between a satellite’s speed and distance from Earth
  Satellites that are close to the Earth orbit quickly
  Satellites that are far away orbit slowly
  Mean Motion is an Average Speed over an Orbit and is measured in revolutions/day

## Slide 10
Keplerian Data
Mean Anomaly provides the position of the satellite along its orbital ellipse at Epoch Time
  Measured as an angle where MA=0 at perigee and MA=180 at Apogee
  Same concept as ‘Phase’
Drag is a measure of the rate at which Mean Motion is changing due to drag or other effects.
  Measured in revolutions/day and is a very small number

## Slide 11
Other Satellite Parameters
Epoch Revolution is the number of times a satellite has orbitted from launch to Epoch Time
Attitude (Bahn Coordinates) is a measure of how the satellite is oriented in space
  Measured from the satellite to the Earth’s Center
  Indicates whether the satellite’s antennas are aimed at the center of the Earth

## Slide 12
Tracking Software
A Tracking Program Can Utilize Keplerian Data to Compute the Position and Velocity of a Satellite for Any Given Time
  Real Time Tracking to determine the Satellite’s Current Position
    Antenna aiming for azimuth and elevation
    Doppler Shift Corrections based upon relative Velocity of the Satellite to the Observer
  Future Predictions of when a Ground Station will be in view of the satellite

## Slide 13
Satellite Tracking Programs
A Variety of Tracking Programs Are Available
A Variety of Platforms are Supported
  IBM PC
  MacIntosh
  Commodore C-64
  HP Calculators

## Slide 14
Satellite Tracking Programs
IBM PC’s Have a Variety of Programs for Various Operating Systems
  DOS
  Windows
  Win-95
  Linux

## Slide 15
Satellite Tracking Programs
AMSAT Offers a Number of Programs
Windows-95 : 32 Bit NOVA for Windows
Windows 3.1: WINSAT/NOVA
DOS
  Instant Trak (VGA)
  Quiktrak 4.0 (CGA)
  Orbits 3.0 (CGA)

## Slide 16
Tracking Program Features
Graphical Display of Satellite Position
Multi-Satellite Display
Print Future Prediction Tables
Video/Memory/Harddrive Requirements
Math Co-Processor Requirements?
Documentation

## Slide 17
Tracking Devices
Various self-contained ‘Black Boxes’ Provide Autonomous Tracking
  TRAKBOX from TAPR
  Sat Trak IV from Kiron
These devices operate independently of a PC and are capable of Steering Rotors and Adjusting Radios for Doppler Shift