## Slide 1
An Introduction to Amateur Satellites
AMSAT
Roy D. Welch, W0SL
Software Manager
AMSAT- North America

## Slide 2
AMSAT
Presentation Outline
An Overview of the Amateur Satellite Program
What is an Amateur Radio Satellite?
Tracking the Satellites
Working the Easy Sats
Sources of Information

## Slide 3
AMSAT
Amateurs in Space
First Amateur Satellite Launched Dec. 1961
Satellites carry a variety of capabilities
Satellites are built by a variety of countries
A variety of organizations have built Amateur satellites (AMSAT, Universities, Private Companies)

## Slide 4
AMSAT
What is an Amateur Satellite?
Like a Repeater
Retransmits what it “hears”
Has Optimized Receivers, Transmitters
Antennas
Great Location!
Enables Small Stations to Communicate over Greater Distances

## Slide 5
AMSAT
What is an Amateur Satellite?
Unlike a Repeater
Has a Moving Footprint!
  Location Changes/Availability Varies
  Frequency Alteration due to Doppler Shift
Full Duplex
  Uplink and Downlink on Different Bands Simultaneously
Multi-mode (CW/SSB/Digital)
“World Wide” Coverage

## Slide 6
AMSAT
Analog Satellites Utilize
“Transponders”
Receives a SEGMENT of One Band
Retransmits EVERYTHING It Hears on Another Band
Inverting Transponders
  Lowest Incoming Frequency is Retransmitted Over the Highest Outgoing Frequency
  Inverts Signal (LSB to USB)

## Slide 7
AMSAT
Digital Satellites Utilize
“Store & Forward BBS”
Receives on one or more fixed frequencies in one band
Retransmits on one fixed frequency in a different band
Uses Broadcast/Connected Protocol for Downlink/Uplink
Has digipeating capabilities

## Slide 8
AMSAT
Available Satellite Bands
Bands Exist from 10 Meters to 24 GHz
70 CM/Two Meters Often Are Utilized
Various ‘Modes’
Shift Towards Higher Frequencies
“Use It or Lose It”

## Slide 9
AMSAT
Satellite Systems
Attitude Control (RCS, Torquing Coils)
Central Computer (IHU)
Communications (Command Rcvr, Ant, Beacons)
Energy Supply (Batteries, Solar Panels, BCR)
Engineering Telemetry (Electronic Sensors, Encoders)

## Slide 10: AMSAT
Satellite Systems (Cont’d)
Guidance and Control (Sun/Earth Sensors)
Environment Control (Mechanical Design, Heat Pipes)
Mission-Unique Equipment (Transponders, GPS, CCD)
Propulsion (Kick Motor, Arc Jet)
Structure

## Slide 11
AMSAT
Satellite Characteristics
Digital/Analog
Orbital Parameters
Frequencies Utilized
“Payload”

## Slide 12
AMSAT
A Wide Variety of Satellites Exist
12 Satellites Currently in Operation
3 Satellites in Orbit Undergoing Test
Digital Store and Forward
FM Repeater 2 Meter/435 MHz
SSB/CW 2 Meter/HF
SSB/CW 2 Meter/435 MHz

## Slide 13
AMSAT
OSCAR Satellites In Service
Satellite Launch Comments
RS-12/13 5 FEB 91 10-15-144 MHz
AO-10 16 JUN 83 SSB/CW Molynia Orbit
UO-11 2 MAR 84 1200 bps AFSK AX-25
AO-16 22 JAN 90 PACSAT
LU-19 22 JAN 90 Packet BBS/Digipeater
FO-20 7 FEB 90 SSB/1200 bps PSK
UO-22 17 JUL 91 9600 bps DFM BBS
KO-25 26 SEP 93 9600 bps DFM BBS

## Slide 14
AMSAT
OSCAR Satellites In Service
Satellite Launch Comments
AO-27 26 SEP 93 FM Analog Satellite
FO-29 17 AUG 96 Digitalker/Transponder
TO-31 10 JUL 98 9600 bps DFM BBS
GO-32 10 JUL 98 9600 bps DFM BBS
PO-34 1 NOV 98 Undergoing Tests
SO-35 23 FEB 99 Undergoing Tests
UO-36 21 APR 99 Undergoing Tests

## Slide 15: Recent Amateur Satellites
SunSAT (SO-35) Launched 23 FEB 99 @ 0230 PST from Vanderburg AFB:
  Has 9600 bps digital store-and-forward BBS
  High Resolution Imaging System (on S-Band)
  FM/FM Analog
UoSat-12 (UO-36) Launched 21 APR 99 @0500 from Baikonur Cosmodrom:
  Carries a Number of Imaging Payloads (Up to 10 Meter Resolution)
  Store and Forward Communications VHF / UHF and an L/S Band Transponder / High Speed Digital Downlink.
  The S band downlink can run at speeds up to 1Mb/s for downloading imaging data, and can also be used as an L/S band analog transponder.
AMSAT

## Slide 16
AMSAT
Future Satellites
ASUSat1 Arizona State FM Repeater/9600 BBS
Launch September 1999
PHASE 3-D Amateur Radio’s Largest Satellite
HUTSAT Helsinki Technology
MOST University of Toronto
SQUIRT1 Stanford
SQUIRT2 Stanford

## Slide 17
AMSAT
Orbital Parameters
Eccentricity-How Circular the Orbit?
Apogee: Point Farthest from Earth
Perigee: Point Closest to Earth
Inclination Relative to the Equator
Keplerian Elements “Describe” the Orbit

## Slide 18
AMSAT
Satellite Categories
EASY Birds
  RS Satellites: RS-11/12, RS-15, RS-16 (Russia)
  Manned Satellites (MIR/SAREX/ISS)
  Dual Use: FO Satellites (Japan)/AO-27 (FM)
Digital Satellites
  Primarily “Store and Forward” Bulletin Boards
  Other Payloads (Cameras/Sensors)
  1200 bps PSK Mode (AO-16, LU-19)
  9600 bps DFM (UO-22, KO-25, GO-32, SO-35)
  1200 bps AFSK (UO-11)
  38.4k and 78.6k bps DFM (TO-31)
DX Satellites
  AO-10
  Phase-3D

## Slide 19
AMSAT
Why Track?
Satellites are Moving Transponders
Need to Predict When the Satellite Will be in Range of your Station
Antenna Pointing/Doppler Correction
Mutual Pass with Other Stations

## Slide 20
AMSAT
Keplerian Data
“Keps” are the Variables Which Describe a Satellite’s Orbit
Keps are Developed by NORAD/NASA
  AMSAT Provides Reformatted Data
Keps are Distributed Worldwide
  Packet Bulletin Boards
  BBS (DRIG, NASA, AMSAT BBS’s)
  Web Sites (www.amsat.org)
  Automatic e-mail receipt from keps@amsat.org
  Publications (AMSAT Journal, OSR)

## Slide 21
AMSAT
Tracking Software
A Tracking Program Utilizes Keplerian Data to Compute the Position of a Satellite at Any Given Time
–Antenna aiming for azimuth and elevation
– Doppler Shift Correction Based Upon Relative Velocity of the Satellite to the Observer
–Future Predictions of When a Ground Station will be in View of a Satellite
• A Variety of Tracking Programs are Available
–Shareware from AMSAT Web Site
–Windows, DOS and Macintosh available from AMSAT

## Slide 22
AMSAT
AO-27
FM ‘Repeater’ Satellite
Uplink 145.850 MHz / Downlink 436.795 MHz
Polar Orbit--2 to 3 workable passes/day
Works in Daylight Only
Operators can use 1-3 Watt HT with Yagi Antenna (such as the Arrow)

## Slide 23
AMSAT
FO-29
Contains Digitalker, Mode JA Transponder, 1200/9600 BPS Packet Capability
When in Digitalker Mode, Transmits on 435.91 MHz FM
Need to Compensate for Doppler
Digitalker Transmits a Short Message
Can be heard with HT with Stock Rubber Duck
May need to rotate rig/antenna for Best Reception
FO-29 Operating Schedule Available from ANS

## Slide 24
AMSAT
Sources of Information
Books
Periodicals
Internet Sites
BBS Sites
AMSAT Area Coordinators
AMSAT Nets

## Slide 25
AMSAT
    General Information Books
AMSAT How to Use Amateur Radio Satellites (7th ed.)
AMSAT Working the Easy Sats (1999)
AMSAT Mode S: The Book
ARRL Handbook
ARRL Radio Amateur’s Satellite Handbook (1998)
ARRL Satellite Anthology

## Slide 26
AMSAT
Books for Specific Satellite Types
Analog Satellites Operating Guide (1998)
AMSAT-NA Digital Satellite Guide (Includes WiSP Install/Setup Instructions.
P3G to P3D
Decoding Telemetry from Amateur Satellites

## Slide 27
AMSAT
Periodicals
AMSAT Journal (Published Bimonthly, distributed to membership)
OSCAR Satellite Report (Harlan Technologies)
Magazines with Satellite Columns:
  QST
  CQ/VHF Magazine
  CQ Magazine
  73 Magazine
  World Radio

## Slide 28
AMSAT
E-Mail Resources from AMSAT
AMSAT News Services (ANS)
KEPS (Keplerian Data)
AMSAT-BB
SAREX
E-Mail is Sent to Your Internet E-Mail Address
  Subscribe by Sending Message to: majordomo@amsat.org
  Instructions Available on AMSAT web Site (www.amsat.org)

## Slide 29
AMSAT
BBS Sites
Eighteen Telephone Sites Nationwide
Satellite Information Available on AOL/CIS
Coverage of Weather, non-AMSAT Satellite Activities
May Require Pre-registration to Gain Access
List of Sites Available from AMSAT

## Slide 30
AMSAT
World Wide Web Resources
http://www.amsat.org
http://www.tapr.org
Links Available to Related Web Sites

## Slide 31
AMSAT
How Do I Get Help?
Local Satellite Operators
AMSAT Nets (HF and VHF)-Listing Available
AMSAT Field Organization (Area Coordinators)
E-Mail (AMSAT-BB)
Hamfest Forums
AMSAT Exhibits/Hamfest Presence

## Slide 32
AMSAT
  AMSAT Field Organization
Area Coordinators: AMSAT’s Ambassadors
150+ Volunteers in USA and Canada
100% Use E-Mail
Have Knowledge/Get Answers
Make Local Presentations/Hamfest Presence
Area Coordinator List Available

## Slide 33
AMSAT
Where Do I Go From Here?
Visit the AMSAT Booth at Hamfests
Determine Area of Interest--Get Additional Information
Utilize the AMSAT Web Site
Contact an AMSAT Area Coordinator
Request a Club Satellite Presentation
Consider Joining AMSAT & Receive the AMSAT Journal

## Slide 34
AMSAT
For More Information
AMSAT-North America
P.O. Box 27
Washington, DC 20044-0027
tel. (301) 589-6062
e-mail: martha@amsat.org
AMSAT Local Area Coordinator
Roy D. Welch, W0SL
908 Dutch Mill Dr.
Ballwin, MO 63011
tel. (636) 391-5323
e-mail: w0sl@amsat.org