KANSAS CITY TRACKER/TUNER
                  Driver Service-Call Functions

                      Version Dated 6/21/88

*******************************************************************************
*                                                                             *
*       This document is in the public domain and may be freely distributed   *
*       and copied. This document should be copied or distributed intact.     *
*                                                                             *
*       Brooks Van Pelt  KB2CST                  41 Acadia Drive              *
*           (609) 751-1018                       Voorhees, NJ  08043          *
*                                                                             *
*******************************************************************************


                             NOTES:
    1) The driver service routines are invoked by performing an INT nn.
       Parameters are expected to be passed to the driver in registers.
       The default interrupt is INT 63H. While 63h is the recommended
       interrupt, this parameter is set at installation and can be varied.

    2) DOS normally fills unused user-interrupt-vectors with 0000:0000,
       which is not a usable processing address. Application programs that
       attempt to invoke the rotor driver when the rotor driver is not
       installed will cause the system to immediately crash. Application
       programs should test for the presence of the driver before trying to
       call a driver interrupt service. The presence of the driver can be
       established by using the driver's software interrupt vector number
       to obtain through DOS the driver's software interrupt processing
       address, adding 10 (0AH) to the displacement, and comparing the
       data at this address to this eight-byte field: "RotorDRV". The
       compare should be case sensitive. If this data is found the driver
       is present.

    3) Time/Target table entries that have expired (the date & time of the
       entry has passed) are deleted when they arrive at the top of the
       Time/Traget table.

    4) The service interrupt to be used to access the driver services can be
       determined from an application program by searching memory from 40:0
       to the application's load point for the this 23-byte string (excluding
       the double quotes): "RotorDRV - SVC Vector Z". The string will be
       located at displacement 0103H from the base segment address of the
       driver. The byte after the last byte of the string will contain the
       interrupt vector number (00h to FFh). This method is not recommended
       as using this method precludes having more than one copy of the driver
       installed and active at a time.
^L
    **************************************************************************
    Function: Read driver status & binary rotor positions

    At Entry: AH=0

    At Exit:  AL contains the status bits. The bits are set as follows...
                80 - =0 if the PC-card is responding to I/O poll correctly
                     =1 if the PC-card is absent or not reponding correctly
                40 - =0 if the controller is enabled
                     =1 if the controller is disabled
                20 - =1 if the ELEV rotor is stalled & has been disabled
                10 - =1 if the AZIM rotor is stalled & has been disabled
                08 - =1 if the ELEV rotor is being moved or needs moving
                04 - =0 if ELEV rotor is being moved to decrease degree setting
                     =1 if ELEV rotor is being moved to increase degree setting
                02 - =1 if the AZIM rotor is being moved or needs moving
                01 - =0 if AZIM rotor is being moved to decrease degree setting
                     =1 if AZIM rotor is being moved to increase degree setting
              BH contains 0 if this is a azimuth-only installation, and 01h if
                 this is an azimuth-and-elevation installation.
              BL contains the signed local-time offset
                     (UTC + local-time-offset = local time)                 
              CH contains the current binary ELEV rotor position (0-255)
              CL contains the current binary AZIM rotor position (0-255)

    **************************************************************************
    Function: Read current slew setting

    At Entry: AH=1

    At Exit:  CH contains the ELEV slew binary value (-25 to +25 degrees)
              CL contains the AZIM slew binary value (-25 to +25 degrees)

    **************************************************************************
    Function: Write new slew setting

    At Entry: AH=2
              CH contains the ELEV slew binary value (-25 to +25 degrees)
              CL contains the AZIM slew binary value (-25 to +25 degrees)
              Note: If either value is invalid the entire command will
                    be ignored.

    At Exit:  No parameters are returned

    **************************************************************************
    Function: Read current position and target position

    At Entry: AH=3

    At Exit:  AX - current ELEV value in degrees (-90 to 269, signed binary)
              BX - current AZIM value in degrees (0-359, signed binary)
              CX - target ELEV value in degrees (-90 to 269, signed binary)
              DX - target AZIM value in degrees (0-359, signed binary)
^L



    **************************************************************************
    Function: Set Target position

    At Entry: AH=4
              CX - target ELEV value in degrees (-90 to 269, signed binary)
              DX - target AZIM value in degrees (0-359, binary)
              Note: If either value is invalid the entire command will
                    be ignored.

    At Exit:  No parameters are returned

    **************************************************************************
    Function: Clear Time/Target table

    At Entry: AH=5

    At Exit: No parameters are returned

    **************************************************************************
    Function: Get Time/Target table data

    At Entry: AH=6
              CX contains the maximum number of table records to be returned
              DX contains the relative table-record number of the first table
                 entry to be returned. The first entry of the table has a
                 relative table-record number of zero. If the relative table-
                 record number is out of range the returned-entry count in
                 CX will be zero.
              ES:[BX] contains the address of where the data should be placed.

    At Exit:  AL contains the driver's current table mode...
                 00=normal
                 01=repetitive-table-processing mode.
              CX contains the number of table entries returned.
              DX if the driver is in BBSROTOR mode, DX contains the relative
                 table entry# of the Time/Target table currently in force.
^L


              
  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  - 

             Normal Table Entry Format For Time/Target Read And Write:
              +0: Word : Year (the full year, eg, 1987) in binary
              +2: Byte : Month in binary (1 to 12)
              +3: Byte : Day of month in binary (1 to 31)
              +4: Byte : Time hour   in binary (0 to 23) (UTC)
                       : This byte can be OR'd with 80H to indicate it is the
                       : first entry of a satellite pass. This is optional.
              +5: Byte : Time minute in binary (0 to 59) (UTC)
                       : This byte can be OR'd with 80H to indicate it is the
                       : last entry of a satellite pass. This is optional.
              +6: Byte : Time second in binary (0 to 59) (UTC)
              +7: Word : Target ELEV in signed binary (-90 to 269)
              +9: Word : Target AZIM in binary (0 to 359)
              +11:BYTEs: 8-byte ASCII satellite identifier. This field MUST be
                         present and accurate in every table entry for a pass.
              +19:L-INT: This field contains the doppler-shifted beacon
                         frequency of the satellite in hertz. It is a 32-bit
                         integer whose most significant byte is in the right-
                         most byte and whose least significant byte is in the
                         left-most byte.

                        Table-entry length = 23 bytes

  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  -  - 

                   Repetitive-table-processing mode Table
                Entry Format For Time/Target Read And Write:

              +0: Word : FFFFh
              +2: Word : Starting minute within cycle period (relative to 0)
              +4: Word : Azimuth for this segment (0-359)
              +6: Byte : Ten-byte ASCII segment description
             +16: Byte : 7-byte unused field

                        Table-entry length = 23 bytes
^L


              
    **************************************************************************
    Function: Add Time/Target table entry

    At Entry: AH=7
              ES:[BX] points to the Time\Target table image to be added to the
                      table. This image is copied during the SVC-call
                      processing and does not need to be maintained after
                      control is returned to the calling program. The formats
                      of the table-entry images are described above in the
                      "GET TIME/TARGET TABLE DATA" section. The driver should
                      be disabled when adding BBSROTOR-mode table entries.

    At Exit:  AL - =0 if the add went ok
                   =1 if a parameter was invalid
                   =2 if the table was full & the entry could not be added

    **************************************************************************
    Function: Read driver's computed date and time

    At Entry: AH=8

    At Exit:  AX contains the years value in binary (1987 = 07C3h)
              BH contains the month in binary (1 to 12)
              BL contains the day of month in binary (1 to 31)
              CH contains the hours value in binary   (UTC)
              CL contains the minutes value in binary (UTC)
              DH contains the seconds value in binary (UTC)
              DL contains the quarter-secs value in binary (roughly 9/8 fast)
^L



    **************************************************************************
    Function: Disable/Enable driver movements. The disable function forcibly
              stops rotor movements and sets the rotor status as disabled.
              The enable function reverses this effect.

    At Entry: AH=9
              AL=0 for disable, =1 for enable

    At Exit:  No parameters are returned.
^L



    **************************************************************************
    Function: Notify driver of pop-up installation. This command is used by
              the TSRs (eg, OSC.COM) during their installation to ensure that
              the TSR is only installed once. THIS FUNCTION SHOULD NOT BE USED
              BY APPLICATION PROGRAMS AS IT COULD INTERFERE WITH THE CORRECT
              INSTALLATION OF THE TSRs.

    At Entry: AH=0Ah
              BX contains the bit-mask value assigned to this program (eg.,
                 OSC.COM uses 0001h)

    At Exit:  AX contains zero if the calling program has not been loaded
                 yet, and 0001h if the program has already been loaded.
              BX contains the driver's version#.

    **************************************************************************
    Function: Set ASCII satellite identifier. This command can be used by
              application programs to set the satellite identifier displayed
              by the OSC status pop-up. This function is entirely optional.
              This function is not needed when tabling satellite position
              entries, as the table structure has a satellite-id field.

    At Entry: AH=0BH
              ES:BX - points to the 8-byte satellite-ID text string.

    At Exit:  No parameters are returned.

    **************************************************************************
    Function: This function places the driver into either normal mode or
              repetitive-table-processing mode. It also acts to clear the
              driver's time/target table, because the table formats for
              the various modes are incompatible.

    At Entry: AH=0CH
              AL=00h - place driver in normal mode.
                 01h - place the driver into repetitive-table-processing mode.
              BX     - Contains the cycle period in minutes when entering
                       repetitive-table-processing mode. Must be less than
                       or equal to 10,080 (decimal).

    At Exit:  No parameters are returned.

    **************************************************************************
    Function: This function returns the number of time-target table entries
              defined within the driver.

    At Entry: AH=0DH

    At Exit:  AX contains the number of table entries defined within the driver
^L



    **************************************************************************
    Function: This function returns the driver's current table-processing mode,
              a pointer to the target ID if mode 1, and the current and period
              values if mode 2.

    At Entry: AH=0EH

    At Exit:  AL contains the driver's table mode (0=normal, 1=repeat)
          * Mode 1 *
              ES:BX - points to the 8-byte ASCII text of the current satellite ID
                      per the text supplied in the last "First of Pass" record.
          * Mode 2 *
              BX contains the cycle period in minutes (1-10080)
              CX contains the current minute# within the cycle.

    **************************************************************************
    Function: This function enables or disables the driver's processing of the
              Time/Target table during clock interrupts. The function has been
              implemented to allow the status pop-up's "spool tbl to disk"
              function to work with an unchanging table.

    At Entry: AH=0FH
              AL=0 means the table-processing function should be disabled.
                =1 means the table-processing function should be enabled.

    At Exit:  AL =0 if the table function was disabled before this call.
                 =1 if the table function was enabled  before this call.

    **************************************************************************
    Function: This function passes a text string to the audible morse-code
              sender imbedded in the rotor driver. The text string must
              consist of ascii characters with a null (00h) terminator.
              Unrecognised characters will be replaced with a space. Multiple
              spaces will be replaced with a single space. A 0FFh byte will
              generate the rising warble used for AOS notification. A 0FEh byte
              will generate the dropping warble used for LOS notification.

    At Entry: AH=10H
              ES:SI - points to the ASCIIZ string.

    At Exit:  No parameters are returned.

    **************************************************************************
    Function: This function controls the morse-annunicator enablement. It can
              also provide the current enablement status.

    GET STATUS SubFunction
        Entry: AH=11h, AL=0FFH
        Exit:  AL=current enablement status (0=dsbl otherwise enbl'd)

    DISABLE MORSE SubFunction (also clears any text queued for sending)
        Entry: AH=11h, AL=00H
        Exit:  AL=prior enablement status (0=dsbl otherwise enbl'd)

    ENABLE MORSE WITH OPTIONS SubFunction
        Entry: AH=11h, AL=00H to 0FEH
        Exit:  AL=prior enablement status (0=dsbl otherwise enbl'd)
^L



    **************************************************************************
    Function: This function forces the driver to enable to morse-annunciator
              and send the status of the driver in CW. The annunciator
              enablement is ignored for this function.

    At Entry: AH=12H
              ES:SI - points to a 22-byte work area used by the driver
                      as a work area.

    At Exit:  No parameters are returned.

    **************************************************************************
    Function: This function forces the driver to delete from the Time/Target
              table the remainder of the satellite pass. If the first entry in
              the table is a start-of-pass record the entire pass is deleted.

    At Entry: AH=13H

    At Exit:  No parameters are returned.

    **************************************************************************
    Function: This function controls the rotor-parking enablement. It can
              also provide the current parking enablement parameters.

    GET PARAMETERS SubFunction
        Entry: AH=14h, AL=00H
        Exit:  BX=Parking delay time in minutes;
                  (0 to 60; 0 means disable parking function)
               CX=Park-position azimuth (0-359)
               DX=Park-position elevation (0-90) 

    SET PARAMETERS SubFunction
        Entry: AH=14h, AL=01H
               BX=Parking delay time in minutes;
                  (0 to 60; 0 means disable parking function)
               CX=Park-position azimuth (0-359)
               DX=Park-position elevation (0-90) 
        Exit:  No parameters are returned; Use GET PARAMETERS subfunction
               to verify operation of this function. The park timer function
               will stopped if it was active when this function was invoked.

    STOP PARKING TIMER SubFunction
        Entry: AH=14h, AL=02H
        Exit:  No parameters are returned.

    START PARKING TIMER SubFunction
        Entry: AH=14h, AL=03H
        Exit:  No parameters are returned.

    **************************************************************************