## Slide 1: Everything You Ever Wanted to Know About Spacecraft Link Budgets . . .
But Were Afraid to Ask.

## Slide 2: Terminology
S/N:
You may have seen it written as: SNR
It’s the “Signal-to-Noise Ratio”
  Signal  Power Level of Signal in Occupied Bandwidth Units: dBW or dBm
  Noise  Noise Power in Occupied Bandwidth or Receiver Filter Bandwidth. Units: dBW or dBm
  So, S/N is dimensionless: Units are in dB

## Slide 3: Terminology
C/N
  C  Power of the signal but, expressed as a carrier with essentially no bandwidth.
  Units: dBm or dBW
  N  Noise power in occupied bandwidth or receiver filter bandwidth. [It’s really QRN ]
  Units: dBm or dBW
  So, C/N is dimensionless: Units are in dB

## Slide 4: Terminology
For Our Purposes:
S/N = C/N
Let’s decide to use the more familiar S/N.

## Slide 5: Exam No. 1
A signal has a received power level of 1 mW and a noise level of 1 W. What is the S/N?
  ANSWER:
  1 mW = .001 Watts
  S = 10 X Log ( 0.001) = 10 X (-3) = -30 dBW
  1 W = 0.000001 Watts
  N = 10 X Log (0.000001) = 10 X(-6) = -60 dBW
  NOW: DON’T DIVIDE -> SUBTRACT:
  S/N = -30 – (-60) = 30 dB NOTE: The “Watts” Cancelled.

## Slide 6: Terminology
C/No or S/No:
  S,C  Signal (or Carrier) Power
  Units: dBm or dBW
  No  Noise Power Per Unit of Bandwidth = Noise Power Density.
    Units: dBm/Hz or dBW/Hz
  S/No  Signal to Noise Power Density Ratio
  Units = dBW/(dBW/Hz) = dBHz
  S/No is the S/N in a 1 Hz Bandwidth

## Slide 7: Terminology
I and Io
  I  All the Power from an Interference Source [QRM]
  Units: dBm or dBW
  Io  Interference Power Density = Power per Unit of Bandwidth.
  Units: dBm/Hz or dbW/Hz

## Slide 8: Terminology
S/(No + Io)
  Signal to Combined Noise Plus Interference Power Density.
  Units: dBHz
  REMEMBER? -- How Do You Add dBs?

## Slide 9
ANSWER: YOU DON’T!
YOU MUST ADD THE TWO “UN-LOGGED” NUMBERS FIRST
YUCK!

## Slide 10
BITCH
. . . Use This Link Model Instead

## Slide 11: Exam No. 2
A signal is received at a power level of –60 dBm. The “white” noise in that receiver’s passband has a density of
-110 dBm/Hz. There is also some interference from a broadcast station that is received at a density of –115 dBm/Hz. What is S/(No+Io)?
ANSWER:
S is free; it’s –60 dBm
To add No and Io we must first “un-Log” the values, add them and “Re-Log” them:
YUCK, Again!

## Slide 12: Exam No. 2 (Continued)
No = -110 dBm/Hz = 1 X 10E-11 milliwatts/Hz
Io = -115 dBm/Hz = 3.16 X 10E-12 milliwatts/Hz
No+Io = (1X10E-11) + (3.16X10E-12) = 1.316X10E-11 mW/Hz
In dB: (No+Io) = 10 X Log (1.316X10E-11) = -108.8 dBm/Hz
NOW:
  S/(No+Io) = -60 –(-108.8) = 48.8 dBHz

## Slide 13: Inserting a Transponder in a Link
USER A
TX
EIRP
RX
G/T
S/C RX
G/T
S/C TX
EIRP
USER B
( )
S/No
UP
(S/No)
DOWN
(S/No)TOTAL

## Slide 14: Who’s Responsible? EIRP and G/T -> That’s Who
CHARACTERISTIC: | ESTABLISHES:
USER EIRP and S/C “G” | S (S/C Received Signal Power)
S/C “T” | No (S/C Received Noise Power Density)
S/C EIRP and USER “G” | S (User Received Signal Power)
USER “T” | No User Received Noise Power Density
UPLINK
DOWNLINK

## Slide 15: The MAGIC Formula!
For a Spacecraft Link Using a “Bent Pipe” Transponder:
(S/No) = 1
1 1
(S/No) (S/No)
+
TOTAL
UP
DOWN

## Slide 16: How Does the Magic Formula Work?
NOTE: It’s the Same Formula as the Parallel Resistor Formula.
(S/No)TOTAL will be  (S/No)UP or (S/No)DOWN, Whichever is Smaller.
For Finite Values of (S/No)UP and (S/No)DOWN, the Total Link Result will ALWAYS be Poorer than the Poorest of the Two Links.
WATCH…

## Slide 17: Exam No. 3
R2= 1 Meg 
R1= 1K 
R total = ?

## Slide 18: Exam No. 3 Result:
R total = 999.0   1K
  The 1 Meg Ohm Resistor had ALMOST NO Effect on the Total Circuit Resistance.
  The Circuit was Dominated by the 1 K Ohm Resistor.
  RTOTAL was LESS than the Smallest Resistor

## Slide 19: Magic Formula Results

## Slide 20: Intermodulation
Distortion Products Produced by the User or Spacecraft Transmitter.
These Distortion Products are Created by Power Amplifier:
  Non-Linear Transfer Characteristics (A)
  Saturation Characteristics (B)
POUT
PIN
A
B

## Slide 21: Two Tone Intermodulation Method (Useful for Narrowband Signal Structures)
fc
f1
f2
2f2 – f1
Signal Amplitude (dBW)
Frequency 
3f2 – 2f1
2f1 – f2
3f1 – 2f2

## Slide 22
fc
f1
f2
2f2 – f1
Signal Amplitude (dBW)
Frequency 
3f2 – 2f1
2f1 – f2
3f1 – 2f2
- 3 dB
Two Tone Intermodulation Method (Useful for Narrowband Signal Structures)
-9 dB [Hard Limiter]
IMR (Two Tone) = 9 dB

## Slide 23
Noise Power Ratio Method (Useful for Wideband Signal Structures)
HPA
fc
Notch Filter
Wideband
Signal
(Bandwidth B)
Amplified
Wideband
Signal
(Output)
Amplifier Input Signal (Test Point)

## Slide 24: Noise Power Ratio Method (Useful for Wideband Signal Structures)
B
fc
- 40 dB
Amplifier Input Signal
Signal Amplitude (dBW)
Frequency 

## Slide 25
B
fc
- 40 dB
Amplifier Output Signal
Signal Amplitude (dBW)
Frequency 
- 15 dB
IMR (Via NPR) = 15 dB
Noise Power Ratio
[ “Slot IM” ] Method

## Slide 26: Want a Copy of the Link Model?
Contact me at:
w3gey@amsat.org